## Slide 1: Analysis and Mitigation of Radiation Induced Errors In Modern Circuits
Dissertation Proposal
Adam Watkins
Advisor: Spyros Tragoudas

## Slide 2: Outline
Introduction
Soft Error Tolerant Latches
Transient Pulse Shape Approximation
Soft Error Simulators
Conclusion

## Slide 3: Introduction
Proposed work entails the analysis of radiation induced errors in circuits
Radiation error occurs when a particle strikes a transistor
Particles come from space or packaging
Many types of particles
  Charged particles (Electrons/Protons)
  Neutrons
  Gamma Rays
  Alpha Particles
  Heavy Ions
  And more
A example of a radiation particle leaving an atom [1].
[1] http://chemistry.tutorvista.com/nuclear-chemistry/radioactivity.html

## Slide 4: Introduction (Cont.)
A radiation particle may create 2 types of error
  Soft Error – The error only causes temporary damage to the device
  Hard Error – The device is permanently damaged
  This work focuses on soft errors
Soft Errors
  Single Event Transient (SET) – temporary voltage pulse
  Single Event Upset (SEU) – a memory element loses is value or a SET is stored in a latch
Soft or Hard Error
  Single Event Latch up (SEL) – a potentially destructive event in which a particle creates a parasitic NPNP bipolar device
Specifically interested in SETs and SEUs

## Slide 5: Radiation Inducing a Soft Error
The radiation exists as a high energy charged particle
The particle travels through the transistor ionizing atoms -generating electron-hole pairs
Causes a break down of the diffusion region in a blocking transistor allowing current to flow
Generates a voltage pulse
May upset the stored data if it occurred in memory
Model of the transistor strike

## Slide 6: Outline
Introduction
Soft Error Tolerant Latches
Soft Error Simulators
Transient Pulse Shape Approximation
Conclusion

## Slide 7: Soft Error Tolerant Latches
In this section existing SEU tolerant latches are investigated
The latches can tolerate 2 types of soft error
  Single Node Upset (SNU) – only a single node is struck by a particle
  Double Node Upset (DNU) – Two Nodes are struck by a particle
Some of the latches are usable to clock gating
  Clock Gating – the clock is set to a stable value to save power

## Slide 8: SEU Tolerant Latch Designs
Most common SEU tolerant latch design is the DICE latch
  Uses 4 cross-coupled elements
Other designs use Muller c-elements to vote on the output
These designs are only capable of tolerating a single error
DICE Latch [1]
Muller c-element [2]
[1] T. Calin et al, Upset Hardened Memory Design for Submicron CMOS Technology, 1996
[2] D. E. Muller, Theory of asynchronous circuits, 1955

## Slide 9: The Double Node Upset (DNU)
DNU - single particle upsets multiple transistors
Particle generates electron-hole pairs in two transistors simultaneously
May lead to the upset of two separate nodes in a latch
Latch will change value if not hardened
Example of a DNU on a latch

## Slide 10: Existing DNU Tolerant Designs
First DNU tolerant design proposed is the DNCS
  Uses two DICE latches and a Muller c-element
Another design is the interception latch
  Uses c-elements connected in a loop
Existing most efficient design is the HSMUF
  Uses an extended DICE element with nodes connected to a Muller c-element
These designs move to a high impedance state after a DNU which limits their applicability

## Slide 11: Clock Gating in DNU Tolerant Latches
Clock gating – shut off the clock to save power
Latches with high impedance states after a DNU may lose their value if gated
Previously a weak keeper on the output used to hold the value for clock gating
Has a high cost in power, delay and area
C-element with a weak keeper on the output

## Slide 12: Proposed Work
Existing latch designs can tolerate both SEUs and DNUs
Many of these designs do not function well when clock gating is used
Use of a weak keeper leads to high delay, power and area costs
It is proposed to develop a DNU tolerant latch suitable for clock gating
The design will not use a weak keeper
Reliability will be ensured through recovery of all nodes after error

## Slide 13: Outline
Introduction
Soft Error Tolerant Latches
Soft Error Simulators
Transient Pulse Shape Approximation
Conclusion

## Slide 14: Soft Error Simulation
This section focuses on discussing current soft error simulators
They calculate the soft error rate of a circuits
Has proven to be a difficult problem
Existing simulators focus on accurate estimation of the logical effect
Many of them suffer from memory blow up or excessive simulation times

## Slide 15: Soft Error Rate
Goal of soft error simulation is to calculate the soft error rate (SER)
  SER = P(e) * Reff * Peff * A
  P(e) – probability of an error on an output
  Reff - effective particle concentration
  Peff - probability of particle hitting sensitive region
  A – area of the circuit
P(e) is difficult to attain due to computational complexity
Can be attained empirically
  Requires testing at a particle accelerator
  The circuit must be fabricated
Leads to a need for accurate and fast simulators

## Slide 16: Evaluation of Combinational Circuits
Increasing error rates has led to increased errors in combinational circuits
Implies that simulators must consider the error in these circuits
Difficult due to 3 masking factors
  Electrical Masking – pulse is attenuated by the gate’s transfer function
  Logical Masking – the “1s” and “0s” mask the pulse
  Temporal Masking – pulse does not meet set up and hold time requirements

## Slide 17: Soft Error Simulation
Soft error simulation consists of 3 parts
Pulse Injection – an equation is used to relate the injected charge to a pulse
Pulse Propagation – pulse is propagated through the circuit
Latching Evaluation – it is determined at the output device of the pulse is stored
Borrowed From: Mitra et al, Robust System Design with Built-In Soft-Error Resilience, 2005

## Slide 18: Multiple Event Transients
Multiple Event Transient (MET) – a single particle strikes two or more cells causing multiple transients
Further complicates the problem due to glitch merging
Logical masking
  The correlation between the propagation functions must be considered
Electrical masking
  Multiple pulses may arrive at a gate simultaneously
A MET generated within a circuit

## Slide 19: Existing Soft Error Simulators
Soft Error Rate Analysis (SERA) Methodology
  Estimates the SER through probabilistic arguments
  Relies on the use of random input patterns
  Uses simple electrical masking models
  Does not consider convergent pulses
Correlation Error Propagation (CEP)
  Determines the SER using the correlation coefficient methodology (CCM)
    CCM – determines the signal probabilities using standard probabilistic arguments with an additional correlation factor
  Uses probabilistic models to determine the SER
  Simple electrical masking calculation
  Considers METs

## Slide 20: Existing Soft Error Simulators (Cont.)
Fast Analysis of Soft Error Susceptibility (FASER)
  Uses binary decision diagrams (BDDs) for logical masking
  Applies partitioning to reduce simulation time
  Electrical masking considered using a simple square shape
  Multiple events are not considered
Modeling and Reduction of Soft Errors in Combinational Circuits (MARS-C)
  Uses BDDs to find logic functions – stored in algebraic decision diagrams (ADDs)
  Capable of simulating many pulses concurrently
  Vulnerable to BDD size blow up
  Can consider METs

## Slide 21: Proposed Work
Current soft error simulators use inaccurate electrical masking models
They are unable to consider METs accurately
Many of them are susceptible to memory blow up or long execution times
It is proposed to develop a simulator that use partitioning and BDDs to determine logical masking
Proposed simulator will also use an accurate model for electrical attenuation

## Slide 22: Outline
Introduction
Soft Error Tolerant Latches
Soft Error Simulators
Transient Pulse Shape Approximation
Conclusion

## Slide 23: Transient Pulse Propagation
This section focuses on estimating the pulse shape in combinational circuits
Accurate pulse shape estimation is important
Most existing pulse approximation methods only consider one pulse arriving on a gate
Additionally only use simple square or trapezoidal approximation

## Slide 24: Transient Pulse Propagation (Cont.)
Pulses are generated at a gate
May be propagated to a gate
If all inputs are non-controlling, it will propagated
A standard pulse has linear and non linear parts
Example of a typical transient pulse
Cases for pulse propagation

## Slide 25: Multiple Event Transients
Increase in the occurrence of METs lead to more pulses
The pulse may arrive at a gate simultaneously
Creates more propagation cases
Assume two pulses arrive at a AND gate
Leads to 3 cases
  Pulse on (a) propagates
  Pulse on (b) propagates
  Both (a) and (b) propagate
Number of cases increase exponentially
3 propagation cases for a 2 input AND

## Slide 26: Existing Pulse Approximation Methods
Simplest existing is square approximation
  Has one parameter – the width
  Calculated from the gate delay
  Very fast and simple
  Not accurate
  Can consider METs by superimposing the inputs pulses
Trapezoidal Approximation
  Has three parameters – rising slope, falling slope and width
  Determined from input pulse parameters
  Fast and simple
  Does not consider the non-linear parts of the circuit
  Not suitable for METs

## Slide 27: Existing Pulse Approximation Methods
Approximation to Distribution Functions
  Can fit to non-linear parts of the pulse shape
  Uses pre-characterized parameters
  Fast and relatively accurate
  Limited in possible pulse shapes
  Not suitable for METs
Equivalent Circuit Approximation
  Uses an equation derived from equivalent circuit
  Iterates through a series of points to form pulse shape
  Fits to gate using pre-characterized look up tables
  Slower but much more accurate
  Does not consider METs
Fitting to Weibull function
Equivalent Circuit Approximation

## Slide 28: Proposed Work
Soft error simulation requires accurate approximation of pulse attenuation
Existing methods only consider a single pulse
No existing methods for multiple pulses
It is proposed to develop a new approximation method that uses an equivalent circuit
The method can accurately estimate the pulse shape for multiple pulses

## Slide 29: Conclusion
Soft errors are a concern in circuit design
New circuit designs and simulation tools are required to handle increasing error rate
For the dissertation the following are proposed
  A DNU tolerant latch suitable for clock gating
  Simulation tool that calculate the SER using BDDs and an accurate electrical masking model
  An accurate equivalent circuit model for determining the pulse shape